## Slide 1
Review and operation
of field equipment &
maintenance
Notes: Courtesy: FAO-Bangladesh Forest Department 2016

## Slide 2
Introduction
Compass
Suunto
GRS densitometer
Diameter tape / Carpenter tape
DME
Truepulse range finder
Soil augers and Soil Cores
Content
Maintenance
GPS
Tablet
Soil Cores

## Slide 3: 1. Introduction
Correct use of instruments and proper data recording are key indicators of a good inventory work
The team leader is responsible for the preparation and maintenance of the equipment
All equipment should be tagged with well marked
Check the condition of the equipment before going to the field
Proper care and maintenance of the equipment must be ensured

## Slide 4
The Tablet is uses to:
  Record field data
  Export field data to the BFI Unit
1. Tablet
Maintenance:
Batteries should be charged every night
The device should be switched off after use
Tip:
The device should be held this way to make data entry easier. The screen rotation can be locked by pressing the button on the side (near the thumb).
Turn on Airplane mode to save battery during daily use

## Slide 5
The GPS unit is used to:
  Navigate to the plot location
  Record coordinates of reference points.
  Determining location of subplots if Plot Centre is not accessible
    Note: Plot coordinates are only provided for plot centre. In case plots centre is not accessible (eg: under water) the distance and bearing function on the GPS can be used.
2. GPS
Maintenance:
Batteries should be remove after use
Batteries should be charged every evening
The device should be switched off after use.
  All coordinates are to be taken with the GPS. The tablet is not used to record coordinates because it is not accurate enough
  The coordinate system used is Degree Decimal
Degree Decimal | Deg/Min/Sec
92.8525245 | 92°53’37”
24.5052585 | 24°43’44”

## Slide 6
2. Compass
The compass’ provided are mirrored to assist accuracy
A compass is used to:
  Record the reference point bearing to the plot centre
  Record the bearing from subplot centre to every tree
Maintenance:
Use only fresh water and mild soap for cleaning the compass
Tip:
  Ensure the red needle is exactly aligned with the red arrow on the base plate
  Ensure the compass is calibrated to magnetic north

## Slide 7
3. Suunto Tandem
Maintenance:
Never attempt to disassemble
Protect from shocks, extreme heat and prolonged exposure to direct sunlight.
stored in a clean, dry environment at room temperature.
Clean with a lightly moistened (warm water) cloth.
The Tandem Sunnto acts as both a compass and a clinometer
The compass is used to measure bearing (as described in the previous slide)
The clinometer is used to measure slope and can also measure height
  Height calculation formula: (a×d)100;
a= angle between top and base reading,
d= horizontal distance
Tips:
  When measuring slope be sure to read the percent measurement (on the right)
  When measuring bearing, read from the top line
    The bottom line provides the reverse angle

## Slide 8
4. GRS densitometer
The Densitometer is used to measure leaf cover
It is operated by looking through the device and recording when the target intercepts with the leaf or sky.
If at least 50% of the ring in the viewing glass is covered by leaves a 1 is counted. If not, it is 0.
Leaf cover is recorded along two 10 m transects. A count is recorded every meter. Therefore the maximum value is 20. The number of “1’ counts is divided by 20 to get the percentage
Maintenance:
Keep densitometer in a sealed plastic bag to protect the lenses from scratching and reduce exposure, dirt and dust.
Do not expose densitometer at high temperatures
After working in rain leave densitometer in a warm dry location overnight
Insert Image

## Slide 9
5. Diameter tape
The Diameter tape is used to measure trunk diameter
Enfold it around the bole of the tree
Where the number "0" aligns with the rest of the tape
Measurement of the tree should be at 1.3 m height (Breast Height)
The diameter can be read directly from the tape
Maintenance:
Don’t apply force to much, it can be stretched.
Wash the steel tape with non-saline water during working in mangroves
Add oil to protect corrosion

## Slide 10
6. Carpenter tape
This used to measures distance between points
The carpenters tape is used in the S Plot and to measure soil depths for example
Open the tape
Fix zero mark of the tape with one object and take the tape to the other object
Take reading and get distance
Maintenance:
Use carefully
Don’t apply to much force between two points of the tape.

## Slide 11
7. Truepulse range finder
Truepulse laser Rangefinder is used to measure distance, slope and height.
Maintenance:
Avoid staring directly at the laser beam for prolonged periods.
Never attempt to view the sun through the scope, this can damage your eyes permanently.
Do not expose the instrument to extreme temperatures.
Tip:
Use the filter and reflector to make sure only the reflector is being targeted.
Ensure the device is calibrated

## Slide 12
8. DME
The DME is used to measure horizontal distance
It is particularly useful for measuring circular plots.
The DME consists of a transponder (A), the DME (B) and a pole for the transponder to attach to (C)
The DME measures the distance between the DME and the transponder
Only one button is used
Maximum range = 30 m (approx)
The DME must be calibrated before use
(C)

## Slide 13
9. Open face Soil augers
Soil Auger is pipe like metallic structure but half portion of this pipe is opened
Augers are inserted vertically into the soil upto a desired level by giving pressure with fixed handle
After attaining desired depth, the auger is twisted around and slowly pull up to get the full core of soil
Maintenance:
Twist the auger slowly otherwise it can bent
After use clean the auger properly
Two types of soil augers are used to take soil samples
  Small auger – in all zones except the Sundarbans (depth to 30cm)
  Long auger – in the Sundarbans (depth to 1m)

## Slide 14
10. Soil Cores
Soil cores are used to collect bulk density samples
  Bulk density provides information about pore space which has implications for plant growth.
  The cores are necessary in order to collect a known volume of soil.
  A pit is dug to reach the desired depth for the core to be taken.

## Slide 15
11. Maintenance
Several ecosystems particularly mangroves are extremely harsh on equipment
All equipment should be cleaned with fresh water and dried with a cloth after every day in the field
This is especially important for steel equipment with screw-on threads; these must be unscrewed and rinsed every day.
Some instruments need battery, so after completing daily works the battery should be removed
When equipment will not be used for an extended period (more than ~3 days), coat the metal parts with a light oil as a protectant
All instruments should be handled carefully
Some instruments are water resistant but not water proof, so if we work in rain then after work the instruments should be dried in sunlight
Before going to the field all necessary instruments should be checked
In case of confusion repetition of measurements can be done

## Slide 16: Thank you