## Slide 1
Bangladesh Forest Inventory 2016
Design
Notes: Courtesy: FAO-Bangladesh Forest Department 2016

## Slide 2
Content
Background: Existing forest inventories in Bangladesh
Objectives: Forest monitoring and assessment
Zones: Definition and zoning
Operation : operational planning
Sampling design: Sampling design, plot shape, inventory protocol
Conclusion

## Slide 3
Background: Existing forest inventories in Bangladesh
In total 17,371 plots have already been measured in Bangladesh since 1958.
9 930 sample plots are still available, out of them
368 510 trees have been inventoried

## Slide 4
NFA
- Rectangle
- 4 sub plots
- Large area
- Less intensity
- 298 plots
- Circular
- Nested
- 17.84m: > 50cm
- 10m: > 20
- 4m: > 5
- 2m: saplings
Protected Area Carbon Inventory
Sal
- Circular
- Cluster
- 3x volume plots
(17.84m)
- 4x area plots
(5.64 – 7.98)
Plot size different depending on location
Sundarban Carbon Assessment
- Circular
- Cluster
- 10m: > 10cm
- 4m: Non-tree veg
- 3m: >10cm
- 2m: Herbs
Background: Example of previous plot designs

## Slide 5
Objectives:
Provide information on current status of forest and tree resources to assist long-term monitoring of natural resources;
Assist national scale management planning, policy decisions and international reporting requirements including REDD+;
Identify links between forest resource use and forest status to assist the valuation of ecosystem services;
Support management objectives within sub-national forest types.

## Slide 6
Sub-National objectives – an example presenting how the data collected would be used to guide actions
Hill | Biodiversity conservation - Bring the barren hills/lands under tree cover through social forestry practice and plantation - Watershed management
Sundarbans | Biodiversity Conservation, Revenue collection from the non-timber forest product, Tourism development
Sal | Reduce deforestation & forest degradation through social forestry, Biodiversity conservation
Coastal | Stabilize newly accreted land through plantation, Bring more lands under plantation to make a coastal green belt to protect lives and livelihoods of coastal community from natural disaster
Villages | Bring marginal land under tree cover; Reduce pressure on the resources of government forest land, Livelihood for marginal and rural community, Encourage and empower women in forestry activities;

## Slide 7
Soil types
Soil salinity
Forest
Water
Zones For Inventory

## Slide 8
The BFI Unit is responsible for the centralization of all information for the national forest inventory, coordination and communication of other national institutions, dissemination of information through the national information system, and reporting.
Five Conservator of Forests (CF) posted in the field will be responsible for checking 5% of the field inventory plots assigned under his responsibility.
Field Inventory Team: 12 Nos-7 members in each
The field team is in charge of the preparation, data collection and providing the data collected to the FI Supervisor/central data base. The field team is composed of: 1 Team Leader, 1 Deputy Team Leader, 1 Technical Expert , 2 Skilled Person and 2 Day Laborers
QA/QC Team: 4 Nos- 4 members in each
QA/QC team is independent, comprising 1 Team Leader, 1 Deputy Team Leader, 1 Skilled Person and 1 Daily Laborer.
Preparation of the field inventory
BFI Unit
Supervisors in Forest division office (FD) – 8 Nos.

## Slide 9
Sampling design: Sampling design, plot shape, inventory protocol
A. Pre-stratified systematic sample with different intensities for each stratum (ecological zone). The sample intensity within each ecological zone will be the same. Post-stratification within each ecological zone will be used to further reduce the sampling error.
B. Precision requirement - specifies the confidence interval width and confidence level for the following parameters: biomass, volume and number of trees of live trees over 10 cm DBH.
C. Subplot types: nested circular subplots by DBH class: 30 cm+, 10-30 cm, 2.5-10 cm, 1-2.5 cm; dead wood transects, and soil samples
D. Total land area, forest land area, % of water.
E. Assessment of the costs for remuneration, transport, equipment etc.
F. Minimize the weighted average variance of the key metric(s) subject to a fixed inventory budget

## Slide 10
All plot location with hexagons
Random selection of plot for each hexagon
Plot within Sundarbans= 278, 105 in water
Sampling Design: Systematic grids and Hexagon on Zones
Grids of 1.5 Latitude X 1.0 longitude were created for all zones
Hexagon drawn on each Zone based on area , forest type, intensity etc
Random selection of a plot from each hexagon
Plots in water not considered

## Slide 11
Zone | Number of plots |  | 
 | On land | On water | Total
Coastal | 113 | 178 | 291
Hill | 429 | 14 | 443
Sal | 145 | 5 | 150
Sundarbans | 173 | 105 | 278
Villages | 998 | 85 | 1083
Total | 1858 | 387 | 2245
No. of Plots to be measured

## Slide 12
Forest zone | Total Area (1000 ha) | Number of plots | Total area of plots (ha) | Sampling intensity (%) | Average distance between plots (km) | 
 |  |  |  |  | Straight line distance | Travel distance along roads
Hill forest | 1714 | 429 | 243.27 | 0.014 | 4.34 | 10.59
Sal forest | 534.8 | 145 | 82.22 | 0.015 | 4.61 | 5.91
Sundarban | 609.2 | 173 | 98.10 | 0.016 | 3.51 | 7.79
Coastal | 1209 | 113 | 64.08 | 0.005 | 6.02 | 11.08
Villages | 10890 | 998 | 565.92 | 0.005 | 6.70 | 13.40
Sampling Design: intensity and average distance between plots

## Slide 13
Technical Design: Circular Plots
(For Hill, Sal, Village & Coastal Plantation)
Cluster of Five sub plots
L plot Radius
is 19 meters
M plot Radius is
8 meters
N
Distance between subplots is 38 m
S plot Radius is 2.5 meters
Cluster of 3 sub plots
For Sundarbans

## Slide 14
Technical Design: Circular Plots
(For Hill, Sal, Village & Coastal Plantation)
Cluster of Five sub plots
Cluster of 3 sub plots
For Sundarbans
N
Distance between subplots centres is 38 m
Subplot
Subplot

## Slide 15
Technical Design: Circular Plot Details

## Slide 16
Trees ≥ 30 cm
19 m
8 m
Trees ≥ 10cm
Bamboo
Dead Wood
2.5m
Seedlings, Nypa palm, Ceriops, phoenix, shrubs etc.
Technical Design: Measurements in each sub plot

## Slide 17
Sustainability of the NFI
Building on existing capacities and needs
Avoiding creating a parallel process
Assumptions
Proposed institutionalization
One NFI unit in BFD
5 Supervisors in 5 locations (Dhaka, Chittagong, Khulna, Sylhet & Bogra)
12 Field teams led by nominated ACF
5 QA/QC teams
One plot in one day
Field campaign during 5 months per year
Complete Hill, Sundarbans and Coastal plantation first
Future
10 Teams, 5 cycle inventory, 20% plots per year
Conclusion

## Slide 18: Thank you