## Slide 1
Bamboo and Seedling Measurements
Notes: Courtesy: FAO-Bangladesh Forest Department 2016

## Slide 2
13. Bamboo data
2. BAMBOO LAND FEATURE
3. BAMBOO SPECIES
  4. BAMBOO Bearing
  5. BAMBOO horizontal DISTANCE
  6. BAMBOO length measurement
  7. BAMBOO Diameter
Content
1. CLUMP RECORD NUMBER
  8. BAMBOO stem number

## Slide 3
13 Bamboo data
13.1 CLUMP RECORD NUMBER
Auto generated.
Will add new clump number for each new input.
BAMBOO DATA:
Recorded for M Plot (radius 8m)

## Slide 4
13.2 BAMBOO LAND FEATURE
In which Land feature the clump is found??
  13.3 BAMBOO SPECIES

## Slide 5
  13.4 Bearing
from the subplot center to the center of the bamboo clump
  13.5 Horizontal DISTANCE
  from the subplot center, to Bamboo clump center.

## Slide 6
  13.6 BAMBOO length
  one measurement that will represent the population average length.

## Slide 7
  13.7 BAMBOO Diameter
  DBH at 1.3 meter
  For averaging, Measure 10 representative samples from the clump
  13.8 BAMBOO stem number
  Number is counted.

## Slide 8
1. What is ‘seedling’ as per BFI manual?
2. Where (L/M/S plots) to measure/ count the seedlings?
3. How to measure/ count the seedlings?
4. Identifying and recording the seedling species
5. Seedling notes
1. Content

## Slide 9
What is ‘seedling’ as per BFI manual?
Seedlings must be at least 10.0 cm in length and less than 2.0 cm at DBH in order to qualify for tallying

## Slide 10
Total Height = at least 10 cm
DBH = < 2 cm
Fig. A seedling in the hill forest of Chittagong

## Slide 11
Layout of plots in (A) Hill, Sal and Village Forests and (B) Mangroves; (C) Subplot details
Where to measure/ count the seedlings?
In S plot of each sub-plot
Total number of subplots in Hill/ Sal/ Village forests = 5, therefore total S plots = 5
For mangroves, total subplots = 3, therefore total S plots = 3
Radius of S plot = 2.5 m
S plot is located at the bearing of 90 degrees and 5 m from the centre of L/M plots

## Slide 12
How to measure/ count seedlings?
Seedlings information is obtained by counting live tree seedlings by species and land class
All live seedlings that have their base inside the S Plot boundary regardless of vigor, damage should be counted
In case of a clump of seedlings/coppices only one seedling which is vigorous should be counted (a clump may consist of 3 or more live stems that sprouted from a common root base including stumps)
Nypa will be recorded as a count

## Slide 13
How to measure/count seedlings?.......cont’d
Count all individual seedlings by species.
When seedlings are distributed evenly on an S Plot, one way of estimating is to count the number of seedlings on one quarter of the S Plot and multiply by four (given that there is only one land feature on the S plot)- repeat for each species.

## Slide 14
Identifying and recording the seedling species
Record the SPECIES code from the Tree Species List
Use the same procedures as the data item found in the Tree and Sapling data
If the species cannot be determined in the field, tally the seedling, but bring branch samples, foliage, flowers, bark, etc. to the office for identification
Make a note to correct the SPECIES code later

## Slide 15: Thanks