## Slide 1
Measurement of tree and sapling attributes
Notes: Courtesy: FAO-Bangladesh Forest Department 2016

## Slide 2
1. Tree attributes for BFI
2. Tree status
3. Species
4. Measurement of tree bearing from plot center
5. Horizontal distance of tree from plot center
6. Diameter and height of stumps
7. Diameter at breast height
8. Tree height measurement
Contents
9. Crown position
10. Tree damage
11. Damage severity
12. Decay class

## Slide 3
1. Tree attributes for BFI
The following attributes needs to assess and measure during BFI
  Tree status
  Species
  Bearing
  Horizontal distance
  Diameter of stumps
  Diameter at breast height
  Total height
  Bole height
  Crown height
  Crown position
  Tree damage
  Damage severity
  Decay class

## Slide 4
Broken and attached more than 50% of the stem, consider as standing tree. Measure the length of the tree including the broken portion
Broken and attached less than 50% of the stem, consider the broken part as coarse wood debris and standing part as damaged standing tree
Broken and attached at below the 1.3 m height = stump
Standing dead tree
Coarse woody debris
  Live tree
  Dead standing tree: The tree is standing above a 45 degree angle; a tree is dead when none of its parts are alive (leaves, buds, cambium) at 1.3m or above.
  Stump (dead)
  Stump (alive)
Record the present status of each targeted trees and stump (top diameter ≥ 10 cm) as following categories
2. Tree status

## Slide 5
3. Species
Record the appropriate species name from the dropdown menu in open foris collect
If the species in not in the dropdown list, consider the following
  Manual input of the species name
  Try to know the local name
  Use “UNK” for unknown species
  Collect the specimen for identification
If the species is known by another (local) name
  Use “OTHER” or “UNK” for unknown species
  List details in the space provided

## Slide 6: 4. Measurement of tree bearing from plot center
Measure bearing of trees from the sub-plot center as follows
  Measure bearing from the magnetic north of each trees using Suunto clinometer
Measurement of tree bearing form sub-plot center
Targeted tree
Suunto clinometer

## Slide 7: 5. Horizontal distance of tree from plot center
Measure the horizontal distance of the tree from the plot center using
  Leaner measuring tape
  Trupulse Laser Range Finder
  DME
Use of leaner measuring tape to measure horizontal distance from the sub-plot center to the tree
In case of sloping ground
Horizontal distance = Slope distance  Cos(σ)
Where σ = slope angle in degrees
Sloping distance = Horizontal distance /Cos (α)

## Slide 8: 6. Diameter and height of stumps
Diameter of live or dead stump should be taken whose height is less than 1.3 m
  Live stumps with coppices will be measured twice
    One for the stump and
    Seedling, or sapling or tree in respective sub-plots
  Diameter will be measured using
    Diameter tape
    Measuring tape or ruler: Measure the longest and shortest axes across the top of the stump and record the average of the two measurements
  Height of stump
    Measure the height of the diameter measuring point for stump
Different categories of stump

## Slide 9
7. Diameter at breast height
Tree diameter at breast height is commonly known as DBH, which is measured at 1.3 m height from the ground level as recommended by FAO
Some of the exceptional situation usually arise in the field to measure DBH. These exceptional situation has been shown in the flowing slides
Figure : Diameter measurement procedure using diameter tape
Tape must be perpendicular to tree

## Slide 12
30 cm

## Slide 14: 8. Tree height measurement
Total height: The height (or stem length) from ground line to the top of green terminal bud
Bole height: The height between ground level and the crown point
Crown point: Crown point is the position of the first crown forming live or dead branch
Different attributes of a tree

## Slide 15
Height measurement using Suunto clinometer
  Step 1: Measure the horizontal distance of the targeted tree from the operator
  Step 2: Looking through the opening, line up the horizontal line with the top of the tree and read off the number from the percentage scale (ignore the sign)
  Step 3: Line up the horizontal line with the base of the tree and again read off the number from the percentage scale

## Slide 16: 10. Tree damage
Record the damage type of trees
  None observed: No damage observed at time of assessment
  Insect: Defoliation caused by insect predation
  Disease: Necrosis or other symptoms of ill health observed (usually on foliage)
  Fire: Defoliation structural damage caused by fire
  Animal: Over grazed
  Wind: Affected by storms
  Suppression
  Human: Human-caused (cultural, logging, accidental, etc.)
  Other: Unknown/not sure/other – includes death from human activity not related to silvicultural and land clearing activity (accidental, random, etc.), roots are undermined by erosion, hit by falling tree(include notes)

## Slide 17: 11. Damage severity
Record the damage severity (if any) of the targeted tree
  Low: Damage is less than 30% of the canopy or trunk; the tree is likely to recover from the damage; the damage is unlikely to affect the longevity of the tree.
  Moderate: Damage is more than 50% of the tree canopy or trunk; the tree may make a partial recovery and the damage is likely to reduce the tree’s natural life expectancy
  Severe: Damage is up to 100% of the tree canopy or trunk; the tree is unlikely to recover from the damage; the trees longevity is significantly affected.

## Slide 18: 12. Decay class
Record the decay class of the dead standing targeted tree
  Most branches present: Original branch structure is present with many fine branches
  Few branches present: Few limbs and no fine branches are present; sound at the base and decay is advancing at the upper bole
  No branches / few stumps only: Predominantly a single trunk, minor stumps, significant decay in all parts of tree

## Slide 19: Thank you